SPECIFICATION OF IL-62М aircraft                СПЕЦИФИКАЦИЯ самолета Ил-62М RA-86552

Date of last  overhaul - 29.08.2003.

Airframe                                                                                   Планер

| Manufacture date Дата выпуска | 1990 y. |
| --- | --- |
| Total life (Hrs/Landings) Назначенный ресурс (часы, посадки) | 35000 h., 7500 land., 20 y. Prolongation to 50000 h., 50 y |
| Total FLT hrs and Landings since new (Hrs/Landings) Налет СНЭ (часы, посадки) | 28860 h. / 4703 land. |
| Total FLT hrs and Landings after last overhaul Налет после последнего ремонта (Hrs/Landings) (часы, посадки) | 9493 h. / 1352 land |
| Date of last overhaul Дата последнего ремонта | 29.08.2003. № 243 ГА |
| Number of overhaul accomplished Количество ремонтов | 2 |
| Time between two overhaul (Hrs/Landings) Межремонтный ресурс (часы, посадки) | 12500 h., 2500 land, till 29.08.11 (Further prolongation on a technical condition becomes every year till 20 y/ 25000h, 5500 land) |

| Engine Type Тип | № 1 D-30KU-2 | № 2 Д-30КУ-2 | № 3 Д-30КУ-2 | № 4 Д-30КУ-2 |
| --- | --- | --- | --- | --- |
| Serial number Серийный номер | 484-225 | 290-217 | 216-106 | 191-214 |
| Manufacture date Дата выпуска | 18.10.85 | 19.06.90 | 28.01.76 | 25.03.91 |
| Date of last major overhaul Дата последнего ремонта | 27.082004 | 30.06.2004 | 30.06.2001 | 26.08.2003 |
| Total life (Hrs) | 20000 h | 20000 h | 20000 h | 20000 h |
| Total FLT hrs since new Hrs Налет СНЭ(часы) | 16135 h/ 3107 Cycle | 13180 h./ 2365 Cycle. | 9568h/1773 Cycle . | 17245 h/ 2895 Cycle |
| Total FLT hrs after last Налет после последнего Overhaul (Hrs/) ремонта (часы) | 4146h/ 684 cycles | 4769h/ 618 cycle | 2235 h., 417Cycle. | 3956 h/ 662 Cycle |
| Time between two overhaul Межремонтный ресурс (Hrs/Years) (часы, годы) | 5000 h/ 905Сycl., 6 y, till 6 000 H, prolongation is spent every calendar year. | 5000h./ 905Сycle., 6 y, till 6 000 H, prolongation is spent every calendar year. | 3000h/543Cycle, 6 y, till 6 000 H, prolongation is spent every calendar year. | 3000h/543Cycle, 6 y, till 6 000 H, prolongation is spent every calendar year. |

All Engines will have a service life extension for one year.

APU									ВСУ

| Type Тип | ТА - 6А |
| --- | --- |
| Serial number Серийный номер | 1136А009 |
| Manufacture date Дата выпуска | 30.01.91 |
| Total life (Hrs) Назначенный ресурс (часы) | 3400 h., 5000 Cycle. |
| Total FLT hrs and since new (Hrs) Наработка СНЭ (часы) | 3026 h., 3239 Cycle. |
| Total FLT hrs and Landings after last overhaul Наработка после последнего ремонта (Hrs) | 836 h., 792 Cycle. |
| Date of last overhaul Дата последнего ремонта | 31.10.2002 |
| Number of overhaul accomplished Количество ремонтов | 1 |
| Time between two overhaul (Hrs/Years) Межремонтный ресурс (часы, годы) | 1010 h., 2500 Cycle.,9 y |

The calendar resource established Ilyushin Design Bureau for this type ACs makes 50 years.

По движкам МРР продляться может до 6 000 часов, продление проводится ежегодно. С КБ и АРЗ по движкам у нас отличные отношения и мы всегда можем помочь в этом.

The average charge of fuel by our plane which has the admission for loading in 33 tons:

- at range of flight of 3000 km and more – about 7 tons / hour, at the maximal loading 33 tons.

Ilyushin Design Bureau gives TBO still IN ADDITION:

- on landings for + 2500 land,

- on hours + 10 000 hours,

- +2 years with the subsequent prolongation on Total life a calendar.

On engines TBO can last till 6 000 H, prolongation is spent every calendar year.

From Ilyushin Design Bureau and factory in the city of Kazan (Russia) and a factory on engines at us excellent relations and we can always help with it.

LIST OF AVIONICS ONBOARD OF IL-62M

The basic equipment of the IL-62M includes all the instruments for altitude instrument flying under IFR as follows:

| Pilot-static and gyro instruments (ICAO standards) | Country of Manufacture | Number of units |
| --- | --- | --- |
| Gyro-magnetic compass system | TKSP-2P | Russian made | 1 unit |
| Magnetic compass | KI-13 | Russian made | 1 unit |
| Navigation system | NV-PB-1 | Russian made | 1 unit |
| Navigation system | KURS-MP-70 | Russian made | 2 units |
| Navigation system | SD-67, SD-75 | Russian made Russian made | 1 unit 1 unit |
| Inertial systems | I-21 | Russian made | 2 units |
| Enhanced Ground Proximity Warning System | SSOS-«Vektor» | Russian made | 2 units |
| Altitude indication and monitoring systems (RVSM) | VBE-2A | Russian made | 2 units |
| Altitude indication and monitoring systems | Altimeter-921 (футомер) | USA | 1 unit |
| Meteorological radar | GROZA-62A | Russian made | 1 unit |
| Radio altimeter | RV-5MD | Russian made | 2 units |
| ADF | ARK-15M | Russian made | 2 units |
| Landing system (operates ILS mode) | KURS-MP-70 | Russian made | 2 units |
| VHF Comm transceiver | BAKLAN-20D (8,33 kHz) | Russian made | 2 units |
| HF Comm transceiver | MICRON | Russian made | 2 units |
| Transponder (operates ICAO standard modes) | SOM-64, SO-70 | Russian made | 1 unit |
| Additional navigation equipment installed |
| TCAS/ACAS-II | TCAS-II | Collins, USA | 1 unit |
| Transponder S mode | TCAS-II | Collins, USA | 1 unit |
| Transponder C mode | TCAS-II | Collins, USA | 1 unit |
| GPS | TNL-2000 Approach Plus | USA | 1 unit |
| Emergency radio beacon («KOSPAS-SARSAT» systems) | ARM-406P ARM-406AC1 | Russian made Russian made | 1 unit 1 unit |

4. Technical Status of the Aircraft

4.1. Rough landing 
What kind of work done                                            
What kind of damage found                                                                                         no

Cases of  aircraft damage by mercury                                                                          not damaged
Indicate the damaged places and the taken measures.

4.2. There were cases of aircraft damage by 
electric discharge and what damaged                                                                           not damaged

4.3.   Number of unpressurized places of cell tanks and location scheme                   no

4.4. Corrosion, cracks, crates                     		                                                    see the Onboard book  
and other external operational damages

4.5. Are there any comments concerning flight operation                                           no

4.6. The state of cable and wiring of                        
Electrical equipment, Defects detected during exploitation                                        no

4.7. Cases of wires damages in Switching devices and communication
boxes and methods of its removing                                                                             no

4.8. Depth of the scratches on the damper support piston of the landing gear            no

4.9. The state of the passenger cabin             	                                                             good

4.10. Where was made last articulation. 		                                                   R-2 Factory 243GA
Deviations points

5. GENERAL INFORMATION

5.1. Commercial loading 	- 23 tons, 174 passengers, available transform to cargo variant 33n, 20 passengers

5.2. Volume - 210м34.

5.3. Dimensions:

Entrance doors - 1.83 х 0.864м

Doors of cargo outlets

№1 - 1.31 х 1.26м

№2 - 1.00 х 1.26м

№3 - 0.7 х 0.76м

№4 - 1.07 х 1.15 х 1.26м

| Crew | 5 |
| --- | --- |
| Cruise speed, km/h | 820-900 |
| Altitude, m | 10000-12000 |
| The maximal range of flight - | 11 000 km. |
| Range with payload of 23000 kg (air navigational fuel reserve=5100 kg), km | 7800 |
| of ISA at the sea level), m | 3300 |
| Landing distance required (in conditions of ISA at the sea level), m | 2500 |
| Maximum takeoff weight, tons | 165 |
| Maximum landing weight, tons | 105 |
| Maximum fuel system capacity, l | 105300 |
| Permissible centrings, ADMC %: |  |
| - maximum-front | 27 |
| - maximum-back | 34 |

- We offer for SALE 1990 IL-62M with TCAS. II categories ICAO.

Date of last  overhaul - 29.08.2003.

| Engine Date of last overhaul | 27.082004 | 30.06.2004 | 30.06.2001 | 26.08.2003 |
| --- | --- | --- | --- | --- |

AC will have a service life extension till August 2011. All Engines will have a service life extension for one year.

Delivery - 40-45 days.

Asking - $1,000,000.00 US.

In the further prolongation annually up to 2013 without OH.

- We offer for SALE 1990 IL-62M with TCAS, EGPWS and Stage 3.

Engines 3 Chapter ICАО on noise available. WE NEED TWO MONTHS OF PREPARATION AND AGREED PRICE FOR INSTALLATION WGPWS, refinement engines and conducting technical work on the extension of the resource prior to August 2011.
We can also install the cargo door for an additional charge or we can give you contacts for the plant to coordinate the installation.

Asking - $1,400,000.00 US.

We also offer 4 x D-30KU-2,  Overhaul - 2004-2005,  after OH – 300 hrs. Price - $1.4M US. ( $350 000US for each ).

We offer for PURCHASE or LEASE-PURCHASE

The instalments of payments till 6 months after an advance payment of 50 % are possible.

Lease - purchase is possible, if we know the Purchaser and will discuss guarantees the lease payments.

Or are we willing to give in installments for 6 months.

The first payment of 50% and the other 50% within 5 months.

For ACMI lease:

1990 IL-62M Stage II. with TCAS. 23 tons, 174 Y, available transform to cargo variant 33t, 20 seats.

- Guarantee - 100 hours per month.

- ACMI - 1500$ per

- for crew 7 per.- 40$ the person per day.

- prepayment – POS/DEPOS.

- prepayment - 2 month.

- Hotel 3 ***, transport, 3 single feed, catering, medical support, visas-on client account.

- With our AOC – deposit 25000US.

- Delivery – 40-45 days after prepayment.

--------------------------------

IL-62M Stage III noise, with TCAS, EGPWS.

23 tons, 174 Y, available transform to cargo variant 33t, 20 seats.

- Guarantee - 100 hours per month.

- ACMI - 1700$ (Excluding the Euroinsurance).

- ACMI - 1850$ (Including the Euroinsurance).

- Delivery – Two Month after prepayment.

-------------------------------------

Second AC with CARGO-DOOR IL-62M Stage III noise, with TCAS, EGPWS. variant 33t, 20 seats.

- Guarantee - 100 hours per month.

- ACMI - 2700$ (Excluding the Euroinsurance).

- ACMI - 2900$ (Including the Euroinsurance).

- for crew 7 per.- 40$ the person per day.

- Delivery – Two Month after prepayment.